Table 2 - Schematic parts

| Part Designation | Part Description |
| --- | --- |
| U1 | LM555 Timer Integrated Circuit |
| U2/U3 | LM1458 Dual operational amplifier integrated circuit (one chip) |
| V1, V2, V3, V4, V5, V6 | +9V alkaline batteries (other batteries can be substituted) |
| R1 | 100 kΩ, 1/4W carbon composition resistor in series with a 1MΩ, 0.5W potentiometer |
| R2 | 1 kΩ, 1/4W carbon composition resistor |
| R3 | 22 kΩ, 1/4W carbon composition resistor |
| R4, R6, R7 | 100 kΩ, 1/4W carbon composition resistor |
| R5, R11 | 10 kΩ, 1/4W carbon composition resistor |
| R13, R17, R19, R21 | 10 Ω, 1/2W carbon composition resistor |
| R8 | 27 kΩ, 1/4W carbon composition resistor |
| R9, R10 | 3.9 kΩ, 1/4W carbon composition resistor |
| R14 | 10 kΩ, 1/4W carbon composition resistor in series with a 1MΩ, 0.5W potentiometer |
| R16 | 100 Ω, 1/4W carbon composition resistor |
| R12 | 33 kΩ, 1/4W carbon composition resistor |
| C1, C2, C4 | 10uF, 50V electrolytic capacitors |
| Q1, Q3, Q6, Q7 | 2N2222 NPN Transistor |
| Q2 | 2N3904 NPN Transistor |
| Bulb1, Bulb2, Bulb3, Bulb4 | screw base lamp, 6.3V, 250mA |